NCSA XDS releaase 2.0 
Jason Ng 5-June-91


XDS V-BUFFER VOLUME RENDERING FEATURE
=====================================




WHAT IT DOES

The V-Buffer volume rendering feature in XDataSlice is a technique for
rendering 3D volume datasets as a transparent or semi-transparent volume.
By specifying some parts of the dataset to be more transparent than others,
it is possible to see through the volume and look at features that might
be previously hidden or occluded.

You achieve this by identifying non-overlapping ranges of values in your
volume dataset, and then assigning a degree of opacity (or transparency)
to each range. XDataslice then takes care of the rest.


EXAMPLE 

A classic example is the volume rendering of a CAT scan of a human head.
By identifying ranges of values for different tissue and bone materials,
and then assigning ain opacity level for each range, a X-ray like image
can be created. Furthermore, by using different values and then creating an 
animation sequence, the effect is one of gradually peeling off outer tissues
tissues to reveal the internal structures.



SUBSTANCES and OPACITY

	A substance is a subrange of values in your dataset. When doing 
volume rendering, you should think of how to divide up the dataset's range of
values (from max to min) into several non-overlapping subranges. In volume
rendering terminology, these subranges are the substances,

	Opacity is a value assigned to a substance.  It is a measure of how much 
you can see through that  substance. It is a real number from 0.0 to 1.0. 
A substance with opacity 0.0 is invisible, like thin air. A substance with 
opacity 0.7 is somewhat translucent, like wax. A substance with opacity 1.0 is 
opaque. 

	As a rule, you assign a low opacity to substances that correspond to
parts of your dataset that are not interesting, or that tend to obscure 
other interesting aspects. Conversely, you usually only assign a high opacity
to a substance that correspond to a part of the dataset that is small or is
normally hidden from view.

	Furthermore, you generally assign a distinct color to each substance,
so that you can differentiate between the different substances in the resulting
rendered image.


HOW TO INVOKE

The vbuffer volume rendering feature in XDataSlice applies only to 3D volume
floating-point datasets.

Such dataset is loaded using the "Load 3D SDS"  option in the XDataSlice Main 
Window. After loading, select the "Planes Along Axes" option (click on the
diamond toggle). This brings up the "Display Mode" window. 

 Click on the "View 3D" diamond button at the lower right corner of this window.
This replaces the 2D option (which is the default) with the 3D option, ie
to perform V-Buffer volume rendering.

In this mode, there are 4 dialogs, ie "X pts", "Y pts", "Z pts" and 
"Substances".  

The "Substances" dialog is very important. You *MUST* always specify this.
It lets you specify the number of substances to use to render your dataset.
The default is 5, but that is probably too many if you're just starting to use
this feature. Try 1 or 2 instead.

The other dialogs scales the final image. For example, "X pts" specifies how
many pixels along the x-axis to expand data value from your dataset into.
The default for each axis is 5. This is generally adequate.

You should then bring up the V-Buffer Window by clicking on the "VBUFF" button.


WHAT YOU MUST DO MINIMALLY

The "VBUffer window is a tall rectangular window, with controls and dialogs in
the upper half, and the display area in the bottom.

Your first task to to specify the opacity, data range and color values for each
substance to apply to your dataset. The current substance being edited is shown
in the upper left box, above the "SET" button. The vertical scroll bar allows 
you to scroll between values of different substances.

For each substance you must enter a value into each of the six dialog boxes in 
the upper left corner:

	"Lower" and "Upper" 
	- the low and high value of the subrange for this substance.
	Both are real numbers, and "Upper" must obviously be greater than "Lower".
	Furthermore, both numbers must be within the data range of your dataset.

	"Opacity" 
	- the opacity of this substance.
	A number between 0.0 (invisible)  and 1.0 (totally opaque).
	
	"Red", "Green" and "Blue" 
	- the red, green and blue components of the color of this substance.
	Each is an integer (0-255). The 3 components are combined to form the
	substance's color. For instance, to define a yellow color, specify
	red as 255, green as 255 and blue as 0.

Do this for each substance.

After entering the values for EACH substance, you must click on the "SET"
button, to enter the values into the substance database. Otherwise, they
will be ignored by the rendering process.


Next, you need to specify which portion of your dataset is to be used
in the rendering process. Use the "Near" and "Far" dialog to specify which
plane for the rendering to begin, and which plane for the rendering to end
with.  Both are integers, and "Far" should be greater than "Near". Also,
both values should be between 0 and the max dimension for that axis.

For example, assuming that you are looking on at the X-Y plane of a 30x40x50
volume dataset. Then there are 50 planes along the z-axis. To render the
entire volume, you should specify near=0 and far=49. The rendering process
is faster if you don't specify the entire volume.

The "Incr" dialog is used to specify which planes to use and which planes to
skip bewteen the near and the far planes. The default is 1, which means use
each plane. If you wish the process to use every other plane instead, specify 
"Incr" as 2.  Specifying a large value for "Incr" is not a bad idea if your
dataset is large and you only want to get an approximation.


Finally you need to specify parameters that affect the lighting:

	"Atten"
	-  refers to attenuation. ie how fast the light becomes dim further
   away from the eye. This is a real number from 0.0 to 1.0. The default
   value of 0.80 is usually adequate. 

	"Gamma"
	- this is an adjustment that can cause the high-end values for a particular
	substance to be much brighter than the low-end valueis for that substance.
	The default of 1.0 gives a harsh, highly contrasted effect, with the low-end
   values of the substance barely visible.  A value of 0.8 gives good results.

	"Amb"
	- refers to ambience, ie how much light there is in the environment. Too 
	little ambience causes the entire image to be dark. Too much ambience causes
	the entire image to be bright, like an overexposed shot. There is no default
   value. A reasonable value to use is the maximum value of your dataset.


After all the parameters are entered, click the "Start" button to start the
volume rendering. The cursor changes to a square cursor, and the number in the
"Near" dialog changes, indicating the plane that is current being processed.
A report of the progress is displayed on XDataSlice's main window.

The resulting rendered image is displayed in the lower half of the VBUffer
window. The image mave be saved as a HDF raster image by clciking on the
"Save" button.

*To start a new rendering, you must remember to reset the "Near" value
by entering the plane number in the "Near" dialog.

-----------------------------------------------------------------------------

HINTS

For a smoother image, click on the "Interpolated" toggle before you
click on "VBUFF".


Getting good results can be an art. It depends on how you choose your 
substances. It is also very sensitive to the ambience, gamma and attenuation 
values.  

Always start with the values suggested. Then modify them in small
increments, one parameter at a time, in order to develop a feel for how
the parameters work. Once you've entered values to produce a reasonably 
acceptable result, you should not change them anymore. Instead, you
should  concentrate on adjusting the ranges of your substances to bring out 
the features of interest.

Start with just 1 or 2 substances, and color each a vivid and distinct
color, eg red and blue. This makes feature differentiation easier in the
earlier stages. Later you can use subtler and more complementary colors.

Finally, remember to record the parameters somewhere. Otherwise, the next
time you want to do a volume rendering on the same dataset, you will
have to go through the entire iterative process again.


SAMPLE DATASET FOR RENDERING

The sample dataset "dnty.hdf" is a good dataset of experimenting with vbuffer
volume rendering. (This is a crystal lattice dataset.)

Sample run:

	 2 substances:
	         lower  upper  opacity     red green blue
	subs 1:  0.11   0.21    0.7        200   0    0
	subs 2:  0.3    0.35    0.4        0     0   80

	attenuation: 	0.8
	gamma: 			0.88
	ambience: 		5

	near plane:	0 
	far plane:	5 
	incr:			1